## Slide 1: EQUIPMENT MANAGEMENT – Preventive MAINTENANCE AND CALIBRATION
MPIA Quality Alliance Webinar Series
Presenter: Mary Johnson
Notes: Hello, Everyone.
Welcome to Webinar # 7 in a series of Quality-related webinars presented by the MPIA Quality Alliance, a sub-committee of the Montana Photonics Industry Alliance in Bozeman, Montana.
Thank you for joining us.
My name is Mary Johnson. I’m CEO of Wavelength Electronics. We design and manufacture the electronics behind precision laser diode systems.
The subject of this webinar is the process for Equipment Management – both Preventive Maintenance and Calibration.

## Slide 2: Agenda: This is what you will learn
Why should I proactively manage and calibrate my equipment?
How can I best set up a Preventative Maintenance / Calibration Plan?
How can I make sure the Plan is being followed & is effective?
What can I do right now?
Notes: Our goal is to give you the structure of an Equipment Management process that you can immediately implement with simple tools after watching this webinar.
First, why should I proactively manage & calibrate my equipment? Maintaining equipment takes time and human resources. Why would I want a plan to proactively service and calibrate tools? If you have a frugal Manufacturing Manager, you need to be able to justify the expense and effort.
Then, how best to set it up. My company manufactures electronics. We have everything from sophisticated robots that place parts on circuit boards, oscilloscopes that test electronic performance, and simple soldering irons. Other Quality Alliance members build lasers. They need to align optics in mechanical housings to spec. I’ll share our experience so you can extrapolate it to your situation.
Third, once the plan is made, how do you make sure the plan is being followed & is effective?
And to finish – what can you do right now? Where do you start?
Let’s start with some definitions.

## Slide 3: Definitions
Preventive Maintenance:
Maintenance performed on a regular basis,
intended to prevent failures or detect
developing failures.
Calibration:
Comparing measurement values delivered
by a device under test with those of a
calibration standard of known accuracy.
Notes: Preventive Maintenance:
This is maintenance performed on a regular basis, intended to prevent failures or detect developing failures.
A plan should include the maintenance action, the frequency it is repeated, and monitoring to detect changes in performance.
An example is changing the oil in your car.
The action is draining the oil, putting the plug back in, replacing the oil filter, and refilling the reservoir with the correct grade of oil for operating conditions.
The frequency is usually defined in number of miles the car is driven or months, whichever is less.
Monitoring is checking the oil level in the reservoir to make sure the engine will stay lubricated during operation.
Calibration:
This is comparing measurement values delivered by a device under test with those of a calibration standard of known accuracy.
For example, we build Laser Diode Drivers that need to deliver a known amount of current to a laser. If I tell a customer it will deliver 5 amps, I need to measure the output with a calibrated multimeter to make sure it performs as expected.

## Slide 4: Why should I proactively manage my equipment?
Preventive Maintenance
  To avoid a production shut down
  Reacting to problems is costly
  Schedule outages at convenient, known times.
  Monitoring detects potential failures before they become issues
Calibration
  To keep assembly processes in spec and avoid scrap
  To give confidence that the product is in spec
  To avoid field failures
To keep production flowing, save money, keep good customer relations, and avoid waste.
Notes: The biggest reason to proactively manage equipment is to avoid a production shut down. If one of my pick-and-place machines goes down unexpectedly, parts can’t be loaded on the circuit boards. My ability to build is crippled. I’m no longer invoicing. Think of the car oil change. If you let it go too long, you may end up in the middle of nowhere on the side of the road with an engine failure. Your road trip is over.
Equally important is that if I’m reacting to a failure, I’m in panic mode. I don’t have time to think of permanent solutions. I can only bandaid the problem and contain its effect. If I monitor the equipment regularly, I’ll know if a belt is starting to fray or if a motor is getting too hot. I can get spare parts coming in. Reacting to failures can cost a lot. Overnight shipping of replacement parts or a plane ticket for a technician to visit will blow the budget.
With our road trip analogy, if the engine seizes because it ran out of oil, you could be paying for a tow, a new engine, and hotel rooms until a rental car becomes available. Regularly changing the oil and checking the level before heading out on a trip avoids future problems.
Another reason to have a plan is that outages for maintenance can be scheduled. This helps in two ways. First, you can choose a down time when the equipment is not being heavily used. Second, you don’t interfere with the production schedule. The scheduler can plan to work around the outage ahead of time.
And finally, proactively monitoring equipment can detect and address imminent failures. We find problems before our customers do.
Calibration can be needed for equipment or measuring devices.
Proactively calibrating keeps assembly processes in spec and avoids scrap.
In addition to electronics test equipment, we need to calibrate the pick-and-place machine any time we replace belts or other parts that wear down with time. When we’re placing a part whose connection centers are half a mm apart, tolerances are critical. If the part is placed off-center, it’s likely the entire assembly will need to be scrapped.
Another example where calibration is important is with CNC machines. They need positions calibrated, so calipers & depth gauges need to be checked for damage and accuracy at regular intervals. If a batch of parts is run and the calipers used during set up were off, the entire batch might not meet spec and need to be scrapped.
Knowing your equipment is calibrated gives you confidence that the product is being built in spec.
Another reason is to avoid field failures. In my earlier example, if the laser diode driver ships but doesn’t produce adequate current, the customer will return it and we’ll get a black eye.
Proactively managing equipment is important to keep production flowing, for good customer relations, and to avoid creating waste.

## Slide 5: How can I best set up a Maintenance Plan?
Make a list of equipment used in Manufacturing Processes
Conduct a risk analysis for every critical piece of equipment
  How likely is an item to fail?
  If an item completely or partially fails, what might happen?
    Will I create scrap?
    Do I have redundancy built in or will production & invoicing completely stop?
    Is there a lead time on replacement parts? How long would the line be down?
    Do I have troubleshooting ability in-house or would I need to bring experts in?
Determine the financial impact of failures
How much revenue do I lose for each day/hour a machine is down?
What is the cost of scrap if a machine is out of tolerance for a day?
What can fail &
how important is it to business success?
Notes: Setting up an Equipment Management plan involves risk analysis and risk mitigation.
First, you need a list of equipment being used. The scope of the list can be the entire company or just Manufacturing. The list should be exhaustive. It’s easier to remove something from the list than it is to notice it the first time it fails. The list can cover anything from computers that need software upgrades to company trucks that need oil changes. You set the criteria for what goes on your list.
Making the list can be as simple as walking around to see what tools people are using.
Looking through my facility, I have machines for solder paste printing, placing parts, reflow ovens. Selective solder machines. Automated Optical Inspection equipment. Soldering irons. Curing ovens. Test fixtures. Power supplies. Servers that hold data.
Once you have collected the comprehensive list, the risk analysis starts.
For each item, evaluate how likely it is that the equipment will fail and the impact of the failure on your business. That’s Risk Analysis: the process of identifying and analyzing potential issues that could negatively impact a business’s ability to fulfill orders. We could devote an entire webinar to that topic, so I won’t dive into it too deeply.
For Wavelength, I consider many factors:
1. Will anything on the equipment wear out gradually with use? Examples include motors, gears, belts, hydraulics, alignment jigs, capacitors in test equipment, circuit boards, cables that bend frequently, mechanical switches
2. Are there maintenance protocols in the user guides? If yes, that’s a good indicator it needs a preventive maintenance plan.
3. Is this line item critical to meeting a published specification? Does it need traceable accuracy? Can its measurements change over time? If yes, it needs a calibration plan.
So, ask yourself this:
How likely is an item to fail? Risk varies with how delicate or complicated an item is.
If an item fails, what might happen?
Will I create scrap? Will misalignments cause lowered yield, more rework, field failures?
Will production shut down? Key to this...
  Do I have redundancy built in or will production & invoicing completely stop?
  Is there a lead time on replacement parts? How long would the line be down?
  Do I have troubleshooting ability in-house or would I need to bring experts in?
Determine the financial impacts of a failure
What revenue will I lose broken down to each day or hour a machine is down.
Will I need to scrap anything, will I spend money on repairs?
What are the reputation impacts of a failure? What would handling RMAs cost?
Get creative with your most cynical team members and brainstorm what could go wrong. Balance that out with the likelihood of those kinds of events and calculate the costs of a failure.
What can fail and how important is it to business success?
For example, on our road trip what can go wrong? Car part failure. Bad weather. Fuel supply. You forget something. What are the risks that matter?

## Slide 6: Maintenance Plan – Mitigate Risk
For each unacceptable risk make a plan to minimize the risk
  Typical preventive measures:
    Keep spare parts on hand
    Follow user guide maintenance protocols
    Monitor equipment performance
Make sure the plan is Good Enough – not Overkill
  Use validation data to refine intervals between refurbishment or repair cycles
  Mitigating all risk is expensive
Notes: Once you know what the risks are, the next piece of the Preventive Maintenance and Calibration Process is making a plan to mitigate those risks.
Consider these typical preventive measures.
I can keep spare parts on hand. I can set up a plan to replace them at intervals. I can follow the owner’s guide maintenance protocols.
I can monitor critical processes where a machine failure will affect the quality of what is produced.
For example, to populate a circuit board, we stencil on solder paste, load the parts with the pick-and-place robot then run the board through the reflow oven to liquefy the solder paste & solder the joints. If any of the 14 oven heating elements is failing, the temperatures will not melt the solder paste, and someone will need to rework all the failed joints by hand with a soldering iron. One bad set of boards through the oven could cost several days in hand soldering, reducing throughput and spiking cost of goods.
To avoid that, we send a known sample through the oven and monitor the actual temperatures against the expected temperatures every week. We also spend the money to have one spare heating element on hand. We can replace the element in four hours then buy a new spare with ground shipping.
For our road trip example, what equipment on the car is critical to operation?
Engine, transmission, tires. Windshield wipers, turn signals, etc.
What can I do to mitigate the risk of failure?
Manufacturer recommended maintenance: Oil changes, belts.
Monitoring: I’m going to check air pressure in my tires and see what tread level is left before I leave. I’m going to get an oil change and check oil level before I head out on the trip.
Am I going to pack spare parts? A spare tire yes. Spare fuses, yes. Spare windshield wipers & belts, probably not. I’m definitely not going to tow a spare engine around with me.
Mitigating all risk is expensive. Consciously choose what risks are acceptable & which need to be addressed by the Equipment Management Plan.

## Slide 7: Follow the plan and evaluate effectiveness
  Make it easy to follow
  Document the maintenance steps and calendar the tasks
  Assign & train a responsible party to complete the work
  Establish metrics and evaluate effectiveness of the plan
Notes: Once you have a plan, it’s critical that your team follows it. Consider addressing these points.
Make it easy to follow.
Make sure you allocate time for the work and money in the budget for replacement parts or consumables.
Document the maintenance steps and calendar the tasks. Write up what needs to be done, take pictures, and store the document. The tasks can simply be listed in a spreadsheet or on a shared Google or Outlook calendar. There is Asset Management software available, too. Keep it simple. The more complicated the process, the more likely people will be to introduce shortcuts to bypass onerous steps or skip filling out forms.
Assign a responsible party to complete the work. If multiple people share the work, it’s easy to let things fall through the cracks.
Then train the responsible party. Make sure that your expectations are clearly communicated. How often does the task need to be done? Are they authorized to replenish spare parts? What budget do they have to work with? Is the task clearly documented? Where do they go if they see something wrong or can’t complete the task?
Finally, someone needs to monitor the effectiveness of the plan. This is where it’s important to have one person who can oversee the entire plan and own the performance metrics.
What kind of metrics are typical?
Overall Equipment Effectiveness is a commonly used metric. Simply put – Overall Equipment Effectiveness identifies the percentage of manufacturing time that is truly productive. An OEE score of 100% means you are manufacturing only good parts, as fast as possible, with no down time. The metrics you use need to make sense for your company.
To make sure the plan is being followed, close the feedback loop. Make sure the work gets done when it needs to be done. Create logs that are dated & initialed for each task & then make time to review the logs regularly.
Track the metrics at known intervals. For example, how many hours was a machine down each month or what was OEE for the month? Were there maintenance budget overruns? You determine what to track and how often.
If the team didn’t hit the metrics, conduct a Root Cause Analysis to determine why and if the process needs to change. Take time to consider if your plan is too aggressive or not aggressive enough.

## Slide 8: Elements of an Equipment Management Plan
Master Equipment List
Documented maintenance or calibration tasks
Task lists with due dates to mitigate risks
Responsible parties to complete the work
Logs to prove each task was completed on time
Metrics to determine plan efficacy
Notes: A good Equipment Management plan will have these six elements at a minimum.
The Master Equipment List
Documented maintenance or calibration tasks
Task lists developed to mitigate unacceptable risks
Someone to do the work
Logs to prove the work was done
System monitoring to determine if the plan is effective. An aggressive plan will reduce risk but cost more. A plan that isn’t aggressive enough will allow problems that could have been prevented.

## Slide 9: Summary: This is what you learned
It is important to proactively maintain and calibrate equipment
Set up a Plan based on comprehensive risk analysis and mitigation
Monitor the Plan to make sure it is being followed and effective
You can start today
“By failing to prepare, you are preparing to fail.”
Benjamin Franklin
Notes: In summary,
A good Equipment Management Plan will keep production flowing, save money, and find problems in-house before they become customer issues.
It is important to proactively maintain and calibrate your equipment.
Set up a plan that evaluates risk to the company and mitigates unacceptable risks.
Monitor the tasks in the plan and whether the plan achieves its goals.
You can start today.

## Slide 10: Contact Information
MPIA Website
https://www.montanaphotonics.org/
MPIA Quality Alliance
https://www.montanaphotonics.org/quality-alliance/
Trainers | Company | Role | Email
Ben Klein | Teledyne FLIR Systems Inc. | Quality Manager | benjamin.klein@teledyne.com
Daniel Juliano | MSU Technology Transfer Office | Director | daniel.juliano@montana.edu
Mary Johnson | Wavelength Electronics | CEO | mary@teamwavelength.com
Steve Birrell | Quantum Composers | CEO | sbirrell@quantumcomposers.com
Conlin Ritter | Quantel/Lumibird | Quality Manager | conlin.ritter@gmail.com
Kurt Borge | Quality Time Montana | Quality Consultant | qtm@q.com
Matt McCune | Autopilot Inc. | President | matt@autopilotdesign.com
Sara Mines | Teledyne FLIR Systems Inc. | Compliance Manager | sara.mines@teledyne.com